# Notes on the LHCb detector
## Vertex Locator (Velo)
- Has 42 half-moon shaped silicon detector elements
- can be positioned at a distance of 5 mm from the IP
- B is created at IP
  Velo can detect decay products
  → indirect measurement of distance between IP and B vertex (1 mm)
- can be retracted to a distance of 35 mm during unstable beam
  prevents radiation damage
  no interference during injection
## Ring Imaging Cherenkov (RICH) detector
- Measures velocity by capturing Cherenkov light
- Cherenkov Light is emitted if a charged particle enters a medium with a higher velocity than the velocity of light in that medium. The effect is similar to the sonic boom. The shape of the cone depends on the particle velocity.
## Magnet
- Lorenz force bends the trajectory of a charged particles (Formel auf Folie)
- with velocity from RICH the mass of the particle can be determent
## Trackers
- Trackers record the trajectory of a charged particle
- This together with the Magnet leads to a Momentum measurement, besides other important kinematic variables like angles.
## Calorimeters
- ECAL elektromagnetic Calorimeter is a sandwich out of lead plates and scintillating tiles. When a particle hits a lead plate, it produces a shower of secondary particles, they excite the material in the scintillators, which emitted UV light proportional to the particles energy
- HCAL hadronic Calorimeter, is a sandwich out of iron plates and scintillating tiles.
## Muon System
- Each station contains chambers filled with a mix of carbon dioxide, argon and tetrafluoromethane
- Muons will react with this gas mixture and wire electrodes detect the results